SEN55 test experience

# Introduction

Having worked with an SPS30 from Sensirion for a longer time, I thought it would be interesting to test and SEN5X. In this document you can find the results of different tests and remarks.

# Starting with SEN-5x

There are different versions of the SEN5x.

The tests in this document have been performed with a SEN55. This looks to be a combination of existing sensors : the SPS30, SGP41 (VOC/NOX)
and an SHT4x Humidity and temperature sensor. Those are connected to an on-board MCU in the SEN55, which communicates with I2C to the outside world. You can not directly interact with those sensors. All communication is handled with the on-board and MCU. There is only a specific set of commands possible, documented in the datasheet.
It looks that Sensirion is planning to extend this approach with the SEN6X: put many sensors in a single housing to make it easier to integrate in a totals solution.

There is a lot of documentation that is available online for the SEN5x. See Appendix A and in the extras-folder of the library

# First impressions

The SEN55 is a small nice looking device. It was packaged in a small plastic bag and no special attention to shipping caution / package was applied. The internal fan looks large compared to the SPS30. While this is mend to be used within HVAC systems, I am missing a possibility to easily mount this (e.g. with a screw). You need to create a mouting bracket yourself with the information provided.

Sensirion has decided to use a different connector than the SPS30. The used connector is ACES 51451-0060N-001 on the sensor’s side, while the corresponding plug is ACES 51452-006H0H0-001. At the time of writing JST GHR-06V-S is compatible and can be used as well. The connector is not part of the standard package and need to be obtained seperate. Also it will require a different cable when trying to perform a firmware update and/or when installing.

The datasheet looks nice and complete, although during testing it was discovered that it is not completely correct/complete. E.g. reading the VOC state information is showing 10 bytes, while it is 8, the product level information is incomplement (8 bytes instead of 2) and the command to obtain the mass/pm/average values is only documented in a later pdf.

A large number of the acceptable instructions are the same between the SPS30 and the SEN55, but not all of them. Next to that there are additional instructions related to temperature, humidity, VOC and Nox.

Unlike the SPS30 for the SEN55 only I2C communication is documented and supported, which does require the select line to be connected to GND. Not sure why this connection is not implemented by default internal in SEN55. The sixth wire on the connector is not used. As with many other I2C sensors external pull-up resistors need to be applied.

To enable a lower power consumption the SEN55 has 2 operating modes, 1) only RHTG information or 2) RHTG + Mass/Pm information. In the later mode the laser will be turned on. This is a nice feature to monitor only on the gas (VOC / NOX) information and perform an analysis with PM information on a regular interval or when the gas values are to high. It looks that Senserion is moving into this direction with including other sensors into a single box (see SEN6x). This will make the monitoring of the air quality and controlling HVAC systems easier.

# First results

The SEN55 was delivered without connection cable, which I sourced external.

Connected the SEN55 to an Arduino UNO-R4. Like with the SPS30 the SEN5x must connected to 5V and as such you need to use the SCL and SDA pins on the board and not the QWICC interface. The later is 3v3 only. Additionaly I added 2 10K pull-up resistors.

Instead of using the Senserion drivers, I started to rework my SPS30 library. The Senserion library looks heavy and only has 1 example.
The reworked SPS30 Example1 is doing basic readings. The Serial number, product name and version info are taken from the SEN55. The version info is actually only the firmware level was decribed. Looking at the Sensirion library I discovered the hardware/protocol. The Library is my SEN55 library.

SEN55-Example1: Display basic values press <enter> to start
Trying to connect.
Detected SEN5x.
Serial number: 1C8C26415594BDE8
Product name: SEN55
Version info:
Firmware: 2.0
Hardware: 5.0
Protocol: 1.0
Library: 1.0

At first the Mass and VOC and NOX values do not make sense :

-------------Mass ----------- VOC: NOX: Humidity: Temperature:
     Concentration [μg/m3] index index % [*C]
P1.0	P2.5	P4.0	P10

0.00	0.00	0.00	0.00	0.00	3276.70	49.55	26.58
3.40	3.60	3.60	3.60	0.00	3276.70	49.54	26.58
3.30	3.50	3.50	3.50	0.00	3276.70	49.55	26.58
3.30	3.50	3.50	3.50	0.00	3276.70	49.54	26.58
3.30	3.50	3.50	3.50	0.00	3276.70	49.54	26.58
3.30	3.40	3.40	3.40	0.00	0.00	49.54	26.58
3.30	3.40	3.40	3.40	0.00	0.00	49.54	26.57
3.20	3.40	3.40	3.40	0.00	0.00	49.53	26.57
3.10	3.30	3.30	3.30	0.00	0.00	49.52	26.57

But if you let it run for couple of minutes :

-------------Mass ----------- VOC: NOX: Humidity: Temperature:
     Concentration [μg/m3] index index % [*C]
P1.0	P2.5	P4.0	P10

4.00	4.10	4.10	4.10	81.00	1.00	61.45	22.28
4.00	4.20	4.20	4.20	83.00	1.00	61.76	22.25
4.10	4.30	4.30	4.30	85.00	1.00	62.02	22.22
4.10	4.30	4.30	4.30	87.00	1.00	62.27	22.18
4.10	4.30	4.30	4.30	89.00	1.00	62.49	22.16
4.10	4.30	4.30	4.30	90.00	1.00	62.70	22.13
4.10	4.30	4.30	4.30	92.00	1.00	62.87	22.10
4.10	4.30	4.30	4.30	93.00	1.00	63.05	22.08
4.10	4.30	4.30	4.30	95.00	1.00	63.19	22.07

The algorithm by default maps the VOC readings to a VOC scale from 1 to 500 where 100 refers to the average condition (see “What is the VOC Index?” for more information) and the NOx values are mapped to a NOx scale from 1 to 500, where everything above 1 is an event (see “What is the NOx Index?” for more information). (source : engineering guidelines sen-5x). There are many documents available from Senserion (and thus in the extras-folder) abouve VOC and NOX values and how to use them.

Pressing <enter> while running example1 you will see the PM Mass/number and average

The PM mass and Number have a bit of the same that it needs time to stabilize.

-------------Mass ----------- ------------- Number -------------- -Average-
     Concentration [μg/m3] Concentration [#/cm3] [μm]
P1.0	P2.5	P4.0	P10	P0.5	P1.0	P2.5	P4.0	P10	PartSize

3.00	3.20	3.20	3.20	20.10	23.70	23.70	23.70	23.80	0.39
3.00	3.20	3.20	3.20	20.10	23.70	23.80	23.80	23.80	0.40
3.00	3.20	3.20	3.20	20.10	23.70	23.80	23.80	23.80	0.40
3.00	3.20	3.20	3.20	20.10	23.70	23.70	23.70	23.80	0.39
3.00	3.20	3.20	3.20	20.10	23.70	23.80	23.80	23.80	0.39
3.10	3.30	3.30	3.30	20.60	24.40	24.40	24.40	24.50	0.40
3.20	3.30	3.30	3.30	21.10	24.90	25.00	25.00	25.00	0.41
3.30	3.40	3.40	3.40	21.70	25.60	25.70	25.70	25.70	0.42
3.40	3.50	3.50	3.50	22.20	26.20	26.30	26.30	26.30	0.42
3.50	3.70	3.70	3.70	23.40	27.70	27.70	27.70	27.70	0.43

After a while it will stabilize :

-------------Mass ----------- ------------- Number -------------- -Average-
     Concentration [μg/m3] Concentration [#/cm3] [μm]
P1.0	P2.5	P4.0	P10	P0.5	P1.0	P2.5	P4.0	P10	PartSize

3.90	4.10	4.10	4.10	26.00	30.70	30.80	30.80	30.80	0.48
4.00	4.10	4.10	4.10	26.20	31.00	31.10	31.10	31.10	0.49
4.10	4.30	4.30	4.30	26.90	31.80	31.90	31.90	31.90	0.49
4.20	4.40	4.40	4.40	27.60	32.50	32.60	32.60	32.60	0.49

Remarks :
Like with the SPS30 some of the results are “calculated”. See document https://sensirion.com/media/documents/B7AAA101/61653FB8/Sensirion_Particulate_Matter_AppNotes_Specification_Statement.pdf, chapter 1.6 :

Therefore, the PM4.0 and PM10 outputs of Sensirion’s PM sensors are estimated from PM0.5, PM1.0 and PM2.5 measurements considering typical aerosol profiles instead of being based on “real” raw data events from large particles.

In the different tests that I have done with the SEN55, only on a rare occassion the PM 2.5. Pm4.0 and PM10 numbers would differ. Normally they are the same. (see later SPS30 compare)

A couple of times during testing the SEN55 would show numbers that are “out-of- sense”.

-------------Mass ----------- ------------- Number -------------- -Average-
     Concentration [μg/m3] Concentration [#/cm3] [μm]
P1.0	P2.5	P4.0	P10	P0.5	P1.0	P2.5	P4.0	P10	PartSize

1825.50	3826.30	5462.40	6214.70	6553.40	6553.40	6553.40	6553.40	6553.40	0.81

Even with a software reset I was not able to get the output back under control. Only removing and reapplying power does the job. Seems the SEN55 is sensitive to a good / stable 5V. But also when starting “cold” the mass number can be sky high and it can really take 30 min before the results look “normal”. But I also observed that it needed a power off/on to get to normal values.

Unlike the SPS30 the number of bytes that are exchanged will fit within the lowest I2C-buffer of 23 bytes. The SEN55 does not communicate in Float’s, but in (unsigned) integers with a scaling factor. That is a good thing.

The information as start-up is confusion and largely out of bounds. In later documentation it is stated that maybe the first 30 minutes should be innored.
# SEN55 / BME280 Temperature reading

The SEN55 is using a SHT4x sensor to measure the temperature. As described in the datasheet and other documents (see appendix A) the fact that is internal and also depending on the way it is placed/positioned in a final solution, the temperature reading might be wrong.

I decided to compare the humidity and temperature results against a BME280.

There are 2 examples. Example3 that will show the result next to each other. You can switch between celcius and Fahrenheit. But even more interesting is example4 where you can change the settings in the SEN55 while comparing the BME280. This overview will use example 4.

When started it will show the results next ot each other:

====================== SEN-55 ================== ================= BME280 ==============
-------------Mass ----------- VOC: NOX: Humidity: Temperature: Humidity Temperature Pressure Altitude
   Concentration [μg/m3] index index % [*C]	[%] [*C] [hPa]	Meter
P1.0	P2.5	P4.0	P10

0.00	0.00	0.00	0.00	0.00	3276.70	51.54	26.08	58.3	23.17	1016	-26.0
2.90	3.80	4.50	4.80	0.00	3276.70	51.55	26.08	59.6	23.18	1016	-25.6
2.90	3.00	3.00	3.00	0.00	3276.70	51.54	26.08	59.5	23.18	1016	-25.6
2.90	3.40	3.70	3.80	0.00	3276.70	51.53	26.08	59.5	23.17	1016	-25.5
3.00	3.50	3.80	4.00	0.00	3276.70	51.52	26.08	59.5	23.17	1016	-26.0
3.00	3.60	3.90	4.10	0.00	0.00	51.51	26.08	59.0	23.17	1016	-25.5
3.10	3.80	4.20	4.30	0.00	0.00	51.50	26.08	59.5	23.17	1016	-26.0
3.30	3.90	4.20	4.40	0.00	0.00	51.48	26.08	59.4	23.18	1016	-25.6
3.50	4.00	4.20	4.40	0.00	0.00	51.47	26.07	59.7	23.17	1016	-26.0
3.60	4.00	4.20	4.30	0.00	0.00	51.45	26.07	59.3	23.18	1016	-26.1
3.70	4.10	4.40	4.50	0.00	0.00	51.45	26.06	59.5	23.16	1016	-25.1

Let it run for 3 minutes :

3.90	4.10	4.10	4.10	87.00	1.00	65.53	21.79	59.4	23.19	1016	-25.6
3.90	4.10	4.10	4.10	88.00	1.00	65.53	21.79	60.2	23.18	1016	-25.7
3.90	4.10	4.10	4.10	89.00	1.00	65.55	21.79	59.5	23.19	1016	-26.0
3.90	4.00	4.00	4.00	90.00	1.00	65.56	21.80	59.4	23.19	1016	-25.8
3.80	4.00	4.00	4.00	90.00	1.00	65.56	21.80	59.5	23.19	1016	-25.8
3.80	4.00	4.00	4.00	91.00	1.00	65.56	21.80	59.5	23.20	1016	-25.7
3.80	4.00	4.00	4.00	91.00	1.00	65.55	21.81	59.4	23.20	1016	-25.9

(watch the VOC /NOX values again !!)

Pressing <enter> will bring up a menu and the displaying values are default

1 Temperature offset	0
2 Temperature slope	0
3 Temperature time	0
4 WarmStart compensation 0
5 Acceleration mode	0
6 Update Sen55 values(MUST do to enable above changes)

7 Cancel & disgard above changes

Following changes are applied immediately:
8 Switch to display Fahrenheit
9 Switch to display in foot

Provide the number. Only <enter> is return. (or wait 10 seconds)

Select 1 and the following menu is shown:

1 Temperature offset	0 range -10..10
Provide the number. Only <enter> is return. (or wait 10 seconds)

You now have 10 seconds to provide an answer. The allowed bandwidth is indicated for each option.
Now enter 2 (to increase the SEN55 reading)
The menu is displayed again, and now you need to input 6 <enter> to save the change to the SEN55.

You will now see
Updated temperature compensation.
Updated warmstart compensation.
Updated Acceleration mode.
================== SEN-55 ====================== ================= BME280 ==============
-------------Mass ----------- VOC: NOX: Humidity: Temperature: Humidity Temperature Pressure Altitude
     Concentration [μg/m3] index index % [*C]	[%] [*C] [hPa]	Meter
P1.0	P2.5	P4.0	P10

3.20	3.40	3.40	3.40	103.00	1.00	64.81	21.99	59.1	23.24	1016	-26.1
3.20	3.30	3.30	3.30	103.00	1.00	63.60	23.99	59.1	23.24	1016	-26.6
3.20	3.30	3.30	3.30	103.00	1.00	62.59	23.99	58.9	23.24	1016	-26.6

The SEN55 displays an increased Temperature, close the BME280. The opposite is works as well.

For the other options see the documentation and information in top of sketch.

# SPS30 & SEN55

According to chatgpt comparing SPS30 and SEN55 :
The SPS30 and SEN55 are both air quality sensors, but they serve different purposes and have distinct features.
### SPS30
- Type: Laser dust sensor.
- Measurement: Specifically designed to measure particulate matter (PM1, PM2.5, PM10).
- Technology: Uses a laser scattering method to detect and quantify dust particles in the air.
- Accuracy: High precision for particulate measurements, making it suitable for environmental monitoring.
- Applications: Commonly used in air quality monitoring systems, HVAC applications, and research environments focused on fine particulate matter.
### SEN55
- Type: Multifunctional air quality sensor.
- Measurements: Can measure a variety of parameters, including temperature, humidity, CO2 levels (*1), and particulate matter (though generally less specialized for PM).
- Technology: Integrates multiple sensing technologies, often using various sensors to capture comprehensive air quality data.
- Accuracy: Offers good accuracy across a range of parameters, though the precision for particulate matter may not match that of the SPS30.
- Applications: Ideal for smart building applications, HVAC systems, and environments where a broad overview of air quality is needed.
### Comparison
- Focus: SPS30 specializes in particulate matter, while SEN55 provides a broader range of air quality metrics.
- Use Cases: Choose SPS30 for detailed particulate monitoring; select SEN55 for a holistic view of indoor air quality.
- Complexity: SEN55 is more complex due to its multifunctionality, while SPS30 is more straightforward, focusing solely on particulate matter.
Depending on your specific needs—whether for detailed dust analysis or comprehensive air quality monitoring—one sensor may be more suitable than the other.
*1. CO2-levels are not in SEN55, but will be in SEN6x

There are also some technical information:

SPS30
- I2C or Serial communication
- I2C address is the same as SEN55
- Needs large I2C buffer ( > 48 bytes)
- Wake and sleep option to save power
SEN55
- Only I2C communication
- Works with small I2C buffer
- I2C address is the same as SPS30
- More sensative to good/stable power supply than SPS30
- has SHT4X and SGP4X sensors integrated
- can start Laser and RHT/G separately or together

When starting example20 to compare:

-------------Mass ----------- ------------- Number -------------- -Average-
    Concentration [μg/m3] Concentration [#/cm3] [μm]
P1.0	P2.5	P4.0	P10	P0.5	P1.0	P2.5	P4.0	P10	PartSize

SEN5x	0.00	0.00	0.00	0.00	0.00	0.00	0.00	0.00	0.00	1.63
SPS30	2.21	3.59	4.60	4.80	12.37	16.17	17.57	17.85	17.89	0.60

SEN5x	2.60	6.60	10.00	11.50	8.30	16.20	20.20	20.90	21.10	1.30
SPS30	2.18	3.13	3.80	3.94	13.09	16.41	17.36	17.55	17.58	0.61

SEN5x	2.30	4.00	5.40	6.00	11.90	16.60	18.30	18.60	18.70	0.84
SPS30	2.18	3.01	3.58	3.69	13.34	16.53	17.35	17.51	17.53	0.63

After 2 hours

    Concentration [μg/m3] Concentration [#/cm3] [μm]
 P1.0	P2.5	P4.0	P10	P0.5	P1.0	P2.5	P4.0	P10 PartSize

SEN5x	1.90	1.90	1.90	1.90	12.30	14.50	14.60	14.60	14.60	0.48
SPS30	1.97	2.08	2.08	2.08	13.43	15.66	15.72	15.73	15.74	0.56

SEN5x	1.80	1.90	1.90	1.90	12.20	14.40	14.50	14.50	14.50	0.48
SPS30	1.87	1.98	1.98	1.98	12.77	14.88	14.95	14.95	14.96	0.56

SEN5x	1.90	2.00	2.00	2.00	12.40	14.60	14.60	14.70	14.70	0.48
SPS30	1.80	1.90	1.90	1.90	12.26	14.29	14.35	14.36	14.36	0.56

# Appendix A: Available documentation

(available online and in the extra-folder of the library)

Datasheet SEN5x
Reduced Power Operation for SEN5x
Engineering Guidelines for SEN5x
Mechanical Design and Assembly Guidelines for SEN5x
Mechanical design-in example for SEN5x & SPS50
Sensor Specification Statement (How to Understand Specifications of Sensirion Particulate Matter Sensors)
REACH- and RoHS – Declaration
Sensirion_SEN5x_Read_Mass_and_Number_Concentrations (not documented in the datasheet)
Temperature Acceleration and Compensation Instructions for SEN5x

Compliance of Sensirion’s VOC Sensors with Building Standards
How can I integrate Sensirion’s VOC and/or NOx sensors into my air purifier?
What is a metal oxide (MOX) sensor?
Is it possible to map the output of a MOX sensor to a norm?
What are oxidizing gases?
What are reducing gases?

What is Sensirion’s NOx Index?
What is Sensirion’s VOC Index?

How can air quality at home be improved?